## Slide 1
Hassan Ali Khan
15030044@lums.edu.pk
System and Networking Research Lab (SysNet)
LUMS
1

## Slide 2
2
Components:
Internet of Things(IoT)
Notes: adasdasd

## Slide 3
3
Sensing Node:
Internet of Things(IoT)

## Slide 4
Applications:
IoT
Water usage sensing
Smart meters
Fire sensors
Air conditioning sensing
AT&T - Connected Car
Tesla cars
Health tracking - JawboneUPS
Fitness Tracker - Fitbit
Smart Watches - iWatchs
Smart waste recycling
Smart street lightning
Smart parking
Internet of Things(IoT)
4

## Slide 5
5
Times(s)
Input Voltage (V)
Mote’s Battery life cycle
Charging
Running
Dead
Lost
Lost
Save State
Operating
Voltage
State Retention Issue
Telosb (with integrated solar panel for energy harvesting) calculating FFT

## Slide 6
  Checkpoint whole RAM and registers
6
Conventional Solution
Drawback:
Time Expensive
Energy Consuming
For CP consistency

## Slide 7
Proposed Solution
7
INCH: Incremental, Near Optimal Checkpointing for Intermittent Computations
- Static analysis
- Instrument memory updating instructions
- Keep record of updated locations
- Minimum number of writes on CP update
- Least CP overhead
Inch
Instrumentation
Instrumented
C-code
Executable
C-code
TinyOS Components
nesC compiler
Block Diagram
msp430-gcc

## Slide 8
INCH-Contd.
8
INCH VS Conventional approach

## Slide 9
INCH-Global Vars. Tracking
9
Code Presented
int a=0,b=0; int main(){ int y=foo(x); if(y<10){ a++; } else{ b=b+1; } …
Code Instrumentation
int a=0,b=0; int main(){ int y=foo(x); if(y<10){ record(&a,sizeof(a)); a++; } else{ record(&b,sizeof(b)); b=b+1; } …

Code example:

## Slide 10
INCH-Stack Tracking
10
INCH VS Conventional approach
Stack Segment
Checkpoint
SP
BP
ST
1st Checkpoint
F1
2nd Checkpoint
F2
F1
F2
3rd Checkpoint
F3
F3

## Slide 11
INCH-Initial Results
11
Radio to counter application:
CP interruption interval = 10s
Notes: Checkpoint size when using an incremental approach (green bars) is significantly less than the complete application size (horizontal dotted line). This graph depicts the results of a simple TinyOS application that displays a counter, received in a packet, on the three LEDs of TelosB. The application is interrupted after every 10 seconds to checkpoint and restore its state.

## Slide 12
12
INCH-Evaluation
Evaluation platform:
Hardware
25O kbps, High Data Rate Radio
MSP430 MC, 10kB RAM
USB Interface
Integrated Temp, Light and Humidity Sensors
Software
Opensource
NesC language
Interrupts based OS
Interfaces for routing, sensing, storage etc.
Test Applications:
Sense
  A typical sensing application that randomly (range: 1ms--10ms) samples a sensor, and calculates the average over an array
  This application repeatedly calculates the FFT on a randomly populated (32 bit) long integer array of size 448 (1792 bytes)
FFT
RSA
  This application repeatedly computes RSA over a randomly populated character array of size 2400 bytes, 60 bytes at time

## Slide 13
13
INCH-Evaluation
Checkpoint Size:
Size-Sense
Size-FFT
Size-Size

## Slide 14
14
INCH-Evaluation
Energy Efficiency:

## Slide 15
15
INCH-Evaluation
Simulation Results :
- Latency & Computation overhead

## Slide 16
16
INCH-Limitations
Additional computations
Ignores state full peripherals

## Slide 17
17
My Role
Interface implementation for INCH
Libraries integration
Generating results on benchmark applications

## Slide 18
18
Thank you

## Slide 19
7
Related Work
Two classes of solution
1st Class
2nd Class
Uses separate memories for normal computations and checkpoint storage
Uses non-volatile storage as their only address space
-
FRAM
-
Examples:
1: MementOS (ASPLOS’11)
Loop-latch
Voltage threshold
2: Hibernus(IEEE’15)
FRAM, Function-return
Interrupt for low voltage
Examples:
1: Quick Recall(ASPLOS’11)
FRAM for process’ computations
Writes only registers during checkpoint
Analysis:
Analysis:
CP size optimization
Rewriting
No CP affirmation
Rewriting
CP size optimization
No flash erase overhead
Less data to be written
Energy(FRAM)>>Energy(RAM)
Data inconsistency

## Slide 20
    Minimize number of writes during checkpoint
    Right time to update the checkpoint
8
Challenges

## Slide 21: INCH Contd.
Work flow and Outputs
  INCH analyzes the code statistically before execution and add the “tracking” call to the code.
  On 1st execution cycle whole RAM in copied on FRAM
  In later executions only the modified memory location are recorded for checkpoint update
  The number of write operations are reduced due to smaller update size and incremental checkpointing.
  Introduces computational overhead of tracking RAM.

## Slide 22: INCH- Incremental Checkpointing for Interruptible Computations
Introduction:
  Computational state is only changed by a few statements
  INCH instrument the source code to record memory locations before the execution of such state-modifying statements.
  Offers a better tradeoff between computations and checkpointing overhead.

## Slide 23: My Role
Interface implementation
Library integration
Generating results on benchmark applications

## Slide 24: Proposed Approach – INCH Contd

## Slide 25: INCH Contd.
Code Presented
int a=0,b=0; int main(){ int y=foo(x); if(y<10){ a++; } else{ b=b+1; } …
Code Instrumentation
int a=0,b=0; int main(){ int y=foo(x); if(y<10){ record(&a,sizeof(a)); a++; } else{ record(&b,sizeof(b)); b=b+1; } …


## Slide 26: INCH Contd.
Stack Optimization:

## Slide 27: INCH Contd.
Stack Optimization:

## Slide 28: INCH-Initial Results
Checkpoint size when using an incremental approach (green bars) is significantly less than the complete application size (horizontal dotted line). This graph depicts the results of a simple TinyOS application that displays a counter, received in a packet, on the three LEDs of TelosB. The application is interrupted after every 10 seconds to checkpoint and restore its state.

## Slide 29: INCH - Detailed Results
Test Applications
  Sense: A typical sensing application that randomly (range: 1ms--10ms) samples a sensor, and calculates the average over an array
  FFT: This application repeatedly calculates the FFT on a randomly populated (32 bit) long integer array of size 448 (1792 bytes)
  RSA: This application repeatedly computes RSA over a randomly populated character array of size 2400 bytes, 60 bytes at time

## Slide 30: INCH - Detailed Results Contd.
Memory Updates:
  Following are the bitmap representations of actual RAM updates over multiple execution,
Bitmap-Sense
Bitmap-RSA
Bitmap-FFT

## Slide 31: INCH - Detailed Results Contd.
Block Updates:
Blocks-Sense
Blocks-RSA
Blocks-FFT

## Slide 32: INCH - Detailed Results Contd.
Checkpoint Size:
Size-Sense
Size-FFT
Size-Size

## Slide 33: INCH - Detailed Results Contd.
Energy Efficiency:

## Slide 34: Limitations
Time of interruption for checkpoint
Additional computations

## Slide 35: Current Research Work
Working to port INCH to other platforms and evaluate another approach for state retention

## Slide 36: Future Work
“When to checkpoint” is still unanswered
Explore another optimal solution to the questions mentioned in challenges part.
“Code path to variables binding”

## Slide 37: Future Work Contd.
In this approach the static analyzer will find all the possible code paths
Total number of modifiable bytes of global data segment in each code path will be calculated
Data structure for particular code paths will hold a list of all the modified memory addresses in that specific path
A call for routine CheckEnergyLeft(nextCodePath) will be added before the execution of any code path and feasibility of checkpoint will be calculated

## Slide 38
Thank you